## Slide 1: A GIS Analysis to Identify Future Study Site Locations in the Cedar River Municipal Watershed, WA
Jenna Forsyth
12/07/09
Chester Morse Lake, Cedar River Watershed, WA
Photo Courtesy of http://www.seattle.gov/UTIL/About_SPU/Water_System/Water_Sources_&_Treatment/Cedar_River_Watershed/COS_002326.asp

## Slide 2: Outline
Introduction
Objectives
Analysis
Results
Conclusions
Questions?

## Slide 3
Owned and operated by Seattle Public Utilities
Provides fresh water for the ~ 1.45 million residents of Seattle
Area: 3,946,330,736.44 sq. feet
Located approximately 34 miles east of Seattle, off Interstate-90
The Cedar River Watershed
Introduction

## Slide 4: Where is the Cedar River Watershed?
Introduction

## Slide 5
Scientific question: What is the effect of forest density and structure on snow accumulation in the watershed?
  Forest density relates to canopy density
  Forest structure relates to forest stand age and type (coniferous vs. deciduous)
What is the Scientific study in the Cedar River Watershed?
Introduction
 |  snow accumulation |  snow accumulation
Canopy Density | Low density? | High Density?
Forest Age | Old/Primary Growth? | Young?
Forest Type | Deciduous? | Coniferous?

## Slide 6
Scientific question: What is the effect of forest density and structure on snow accumulation in the watershed?
  Snow accumulation in forested areas such as the Cedar River Watershed, largely depends on how much snow is intercepted or “stuck” in the trees.
What is the Scientific study in the Cedar River Watershed? Continued…
Introduction

## Slide 7
What is the Scientific study in the Cedar River Watershed? Continued…
Introduction
(a) Turbulence within the forest canopy causes variability in how snow is deposited.
(b) Snow intercepted in the canopy sublimates, or falls to the ground.
(c) Interception between different species of conifers is not significant, but
(d) Interception in conifers is significantly greater than interception by deciduous trees.
(e) Because of interception, 20-45% more snow accumulates in clear-cut areas or clearings.
(Graphics from Mark Williams, CU Boulder)

## Slide 8
Three coniferous forest sites of ~ 50x50meter plots
What and where are the current study sites?
Introduction

## Slide 10: What are the forest and topographical characteristics of the sites?
 | Elevation (feet) | Slope (degrees) | Aspect (cardinal direction) | Canopy Density (percentage) | Forest Age (years)
Site 1 | 1,731- 2,207 | 0-11.077 | West | 90-100 | 54
Site 2 | 1,731- 2,207 | 0-11.077 | South | 90-100 | 54
Site 3 | 2,207 - 2,676 | 0-11.077 | North | N/A | Old Growth
Introduction

## Slide 11: What are the objectives of the current GIS analysis?
Locate 3 potential sites to be pairs for the current sites:
  Similar forest and topographical characteristics
    Elevation
    Slope
    Aspect
    Canopy Density
    Forest Age
  Easily accessible (within 100 feet, but no more than 1,000 feet from the nearest road)
  Not overlapping with lakes, streams, or pre-existing study sites or meteorological stations
Objectives

## Slide 12: How was this accomplished?
Elevation
  Reclassified to include only elevations of interest, then new layers with only those elevations for each site
Analysis

## Slide 13
Slope
  First calculated slope ranges from elevation
  Second, analyzed similar to elevation technique, reclassified and created a new layer: slope range equal for all sites
Analysis
How was this accomplished?

## Slide 14: How was this accomplished?
Aspect
Analysis

## Slide 15: How was this accomplished?
Canopy Density
Analysis

## Slide 16: How was this accomplished?
Forest Age
Analysis

## Slide 17: How was this accomplished?
Buffer within a buffer
  New site>100 feet from road but <1,000feet
Analysis

## Slide 18: New potential sites?
Intersected above layers
  New Site 1 Potential Area: 5,368,861 sq. feet
  New site 1
    At least 28,632.02 sq. feet in area (5x5 cells)
    1,854 feet from previous site (skiing)
    8,158.4 feet from previous site (along the road)
New Site 2 Potential Area: 4,273,018 sq. feet
  New site 2
    At least 28,632.02 sq. feet in area (5x5 cells)
    7,532.67 feet from previous site (skiing)
    8,035.22 feet from previous site (along the road)
New Site 3 Potential Area: 1,458,128 sq. feet
  New site 3
    Not possible due to overlap with current site area
Results and Conclusions

## Slide 19
Site 3 Not Possible
Results and Conclusions

## Slide 20: Site 3: Re-calculating Potential New Site Area
Tried with new parameter ranges for elevation, slope, and aspect:
 | Elevation (feet) | Slope (degrees) | Aspect (cardinal direction) | Canopy Density (percentage) | Forest Age (years)
Potential Site 3 Pair | 1,731- 2,676 (DIFFERENT) | 0-17.09 (DIFFERENT) | North, East, or West (DIFFERENT) | N/A (SAME) | Old Growth (SAME)
Results and Conclusions

## Slide 21
  New Site 3 Potential Area: 7,528,051.11 sq. feet
  New site 3
    At least 28,632.02 sq. feet in area (5x5 cells)
    6,433.21 feet from previous site (skiing)
    14,415.37 feet from previous site (along the road)
Site 3: Success!
Results and Conclusions

## Slide 22
Site 3: Success!
Results and Conclusions

## Slide 23: Questions?
Questions?
N
New Site 2
New Site 1
New Site 3

## Slide 24
Thank You