## Slide 1: Ideal Locations for Wind Power Generation in Washington State

## Slide 2: Background
We have been hired by an entrepreneur to locate areas within Washington State suitable for a small wind farm.
  A small number of turbines (<25)
  Low construction costs
  High potential for energy and subsequent revenue generation

## Slide 3: Location Specifications
Land Use that would feasible for construction of wind turbines:
  Bare ground
  Agriculture or
  Non-forested land

## Slide 4: Land Cover

## Slide 5: Wind Power Generation Potential
Outstanding to Superb wind power density
  > 600 W/m2 at a tower height of 50 m
  This number is based upon multiple features including: wind speeds, terrain, and climate.
  Ridges High Points Funneling Points

## Slide 6: Wind Power Generation Potential

## Slide 7: Outstanding to Superb Wind Power Classification and Suitable Land Cover Intersect

## Slide 8: Proximity Requirements
Stay at least 10 miles away from existing wind farms
Within 5 miles of transmission lines
Within 5 miles of state highways

## Slide 9: Transmission Lines, State Highways, and Current Locations

## Slide 10: Other Exclusions
National Parks
All Washington State Mountain Ranges
  Cascade Mountains
  Blue Mountains
  Olympic Mountains

## Slide 11: Final Possible Locations

## Slide 12: Selected Location
Site with maximum area ~.5 square miles
Undeveloped area within Inner Olympic Peninsula
~1.5 miles west of Highway 101
South of the town of Quilcene
With a length of approximately 3.5 miles, the site’s unique shape allows for a high number of wind turbines to be installed along the ridge

## Slide 13: Selected Location Wind Power Generation Potential

## Slide 14: Selected Location Proximity to Roads and Transmission Lines

## Slide 15: Final Location

## Slide 16: Final Location

## Slide 17: Expected Power Generation
50m wind turbines are to be used (rated at 750 kW)
They will be spaced at least five 50 meter rotor diameters apart.
Therefore, we could fit at most, 22 turbines in a line along the 3.5 mile ridge

## Slide 18: Power/Revenue Generation
Assuming a 40% power capacity factor
  This is on the high end because the site is particularly favorable
The site could potentially generate 6.6 MW of power which equates to about 57,800 MW*h over the course of one year

## Slide 19: Data Sources
Washington State Geospatial Data Archive (WAGDA)
  wagda.lib.washington.edu/data/geography/us/vector/
Washington Department of Fish and Wildlife GAP Data Products
  http://wdfw.wa.gov/wlm/gap/landcov.htm
Washington State Department of Transportation (WSDOT) GeoData Distribution Catalog
  http://www.wsdot.wa.gov/mapsdata/geodatacatalog/default.htm#main
National Renewable Energy Laboratory
  http://www.nrel.gov/gis/

## Slide 20: Questions?