## Slide 1: Crossing Lake Washington
Addition of a Third Bridge
Aaron Knight
Stephen Lau
Source: http://commons.wikimedia.org/wiki/File:Aerial_view_of_I-520_bridge_across_Lake_Washington_in_Seattle.jpg

## Slide 2: Objectives
Connect I-5 to I-405
Minimize impact on existing housing and businesses
Connect areas of greatest density
Use the most effective bridge span length
Minimize impact on recreational areas
Minimize impact on wetland areas
Provide available Park & Ride Service
Minimize impact on school or historical sites
Suit the land topography

## Slide 3: Project Area
Source: Google Earth

## Slide 4: Data Evaluated
Data Type | Source
Highway Network | WSDOT
Cities | King County
Water Bodies | King County
Parcels | King County
2000 Census Blocks | King County
Wetlands | King County
Parks | King County
Schools | King County
Historical Sites | King County
Park & Rides | WSDOT
Topography | UW ESS

## Slide 5: Alternatives
North Crossing
South Crossing

## Slide 6: North Crossing
Length of Segment: 6.42 Miles
Length of Bridge:0.9 Miles
Parcels Within 250’: 995
Average Density, 10 miles: 7553 per/mi2

## Slide 7: North Crossing
Within 500’:
Wetlands: 0
Parks: 2
Schools: 3
Historical Sites: 0
Park & Rides: 2

## Slide 8: North Crossing
Topography information:
Significant elevation change, tunnel required

## Slide 9: South Crossing
Length of Segment: 4.62 Miles
Length of Bridge: 2.74 Miles
Parcels Within 250’: 287
Average Density within 10 miles: 6740 per/mi2

## Slide 10: South Crossing
Within 500’:
Wetlands: 0
Parks:1
Schools: 3
Historical Sites: 0
Park & Rides: 2

## Slide 11: South Crossing
Topological information:
Relatively constant elevation

## Slide 12: Comparison
 | North Crossing | South Crossing
Segment Length (mi) | 6.42 | 4.62
Bridge Length (mi) | 0.9 | 2.74
Parcels Within 250’ | 995 | 287
Average Density (per/mi2) | 7553 | 6740
Wetlands within 500’ | 0 | 0
Parks within 500’ | 1 | 2
Schools within 500’ | 3 | 3
Historical Sites within 500’ | 0 | 0
Park & Rides within 500’ | 2 | 2

## Slide 13: Preferred Alternative
Shorter Roadway
No tunnel required
Less parcel acquisition necessary
Reduces congestion for
I-405 in Renton

## Slide 14: Resources
UW ESS Department http://gis.ess.washington.edu/data/raster/tenmeter/byquad/index.html
King County GIS https://wagda.lib.washington.edu/DATA/geography/wa_counties/king/index.html
WSDOT http://www.wsdot.wa.gov/mapsdata/geodatacatalog/default.htm