## Slide 1: Sammamish-Juanita 115 kV Project Route Siting Project November 2012
Gene Lohrmeyer
GeoEngineers
Notes: 1

## Slide 2
GeoRoute Selection Model

## Slide 3
GeoRoute Selection Model

## Slide 4: PSE Needs
GeoRoute Selection Model
Help determine preferred route between substations – need alternatives
Demonstrate and defend route selection process in public meetings

## Slide 5: Issues
GeoRoute Selection Model
Multiple competing values
  Engineering
  Community
  Environment
Other non-GIS efforts by PSE resulted in no consensus
  Professional Judgement
  Criterium

## Slide 6: How would you help PSE with this problem?
GeoRoute Selection Model

## Slide 7
GeoRoute Selection Model
Develop a geoprocessing model
  Combine datasets using weighted overlay tool
  Least cost path analysis using distance tools
    Accumulated Cost
GeoEngineers Solution

## Slide 8: What is Geoprocessing?
GeoRoute Selection Model
Allows you to automate GIS tasks and perform spatial analysis and modeling
Everything in the toolbox can be used in a geoprocessing model

## Slide 9: Geoprocessing Example
GeoRoute Selection Model
20 datasets from various sources
Reproject and clip each dataset to a project boundary

## Slide 10: Weighted Overlay Tool
GeoRoute Selection Model
Allows you to combine rasters of varying importance
  Why rasters?
  Scale (in = 10, out = 0)

## Slide 11: GeoRoute Tasks
GeoRoute Selection Model
Collect existing jurisdictional GIS Data
  Kirkland, Redmond, Dept of F&W
Clip to project boundary and convert to raster
Assign data to either Built, Natural Environment, Engineering or Opportunity groups
  More flexibility for analyzing alternatives
Weighted Overlay Tool
  Weight and combine datasets in each group
  Weight and combine Built, Nat Env and Eng groups (Avoidance Areas)
  Weight and combine Avoidance Areas with Opportunities
Distance Tools
  Least Cost Path Analysis

## Slide 12: Model Overview
GeoRoute Selection Model
Conceptual

## Slide 13
GeoRoute Selection Model

## Slide 14
GeoRoute Selection Model
Built
Environment

## Slide 15
Built Environment Data Layers
Data Reviewed, Within Study Area | Data Reviewed, Not Within Study Area
Single Family Residential Zoning | Cultural/Historic Resources
Multi Family Residential Zoning | Areas of property disputes
Urban Recreation Zoning | Open space taxation parcels
Parcel Size < 5 acres | Airports
Local Parks | Scenic Highways
Native Growth Protection Areas | Surface Mining
View Corridors (Redmond) | Parcels Fronting Local Access Streets
GeoRoute Selection Model

## Slide 16
GeoRoute Selection Model
Single Family Residential Zoning

## Slide 17
GeoRoute Selection Model
Schools and Parks

## Slide 18
Natural
Environment
GeoRoute Selection Model

## Slide 19
Natural Environment Data Layers
Data Reviewed, Within Study Area |  | Data Reviewed, Not within Study Area
Wetlands | Shoreline Jurisdiction | WA Natural Heritage Program areas
Landslide Hazards | Lakes | 
Seismic Hazards | 100 year floodplain | 
Erosion Hazards | Contiguous Tree Canopy | 
Streams |  | 
Steep Slopes >40% |  | 
Sensitive Species (WDFW) |  | 
GeoRoute Selection Model

## Slide 20: Wetlands
GeoRoute Selection Model
Wetlands

## Slide 21
GeoRoute Selection Model
Landslides

## Slide 22
Engineering
GeoRoute Selection Model

## Slide 23
Engineering Data Layers
Data Reviewed, Within Study Area | Data Reviewed, Not Within Study Area
Curved Streets | BPA Crossing
Structures within 15’ of R/W | 
Parcels not adjacent to Public R/W | 
Interstate Highway Crossing | 
Steep Slopes >40% | 
Future WSDOT Improvement Areas | 
GeoRoute Selection Model

## Slide 24
GeoRoute Selection Model
Street Curves

## Slide 25
GeoRoute Selection Model
Steep Slopes >40%

## Slide 26
Built Environment Data Layers Weights
Data Reviewed, Within Study Area | Weight (%)
Single Family Residential Zoning | 20
Multi Family Residential Zoning | 15
Urban Recreation Zoning | 10
Parcel Size < 5 acres | 7
Local Parks | 8
Native Growth Protection Areas | 15
View Corridors (Redmond) | 5
Schools | 10
Native Growth Protection Easement | 15
WSDOT Improvements | 10
GeoRoute Selection Model

## Slide 27
GeoRoute Selection Model

## Slide 28
34%
33%
33%
GeoRoute Selection Model
Combined and weighted avoidance groups

## Slide 29
Built Environment Criteria
100%
0%
0%
GeoRoute Selection Model

## Slide 30: Model Overview
GeoRoute Selection Model

## Slide 31
GeoRoute Selection Model

## Slide 32
Opportunities Data Layers
Data Reviewed, Used for Modeling | Data Reviewed, Not Used for Modeling
Commercial/Industrial Zoning | Open Vegetative Cover
Arterial Street | Community Plan Compatibility
Trails R/W | 
Railroad R/W | 
Parcel size > 20 acres | 
Existing PSE Rights-of-Way | 
Existing Overhead Distribution | 
GeoRoute Selection Model

## Slide 33
GeoRoute Selection Model
Arterial Streets
Notes: Joanne gives presentation on GeoRoute model
Note: copy of GeoRoute Model public involvement poster will be in the AG’s meeting packets
Example map of things we are trying to avoid
Environmental Example
Landslide Hazards (+ study area map)

## Slide 34
GeoRoute Selection Model
Industrial/Commercial Zoning

## Slide 35: Model Overview
GeoRoute Selection Model

## Slide 36
%
%
GeoRoute Selection Model

## Slide 37
GeoRoute Selection Model
Least Cost Path Model

## Slide 38
GeoRoute Selection Model
Full Model

## Slide 39: Alternate Routes
GeoRoute Selection Model
Alternatives can be created by adjusting weights of avoidance rasters
  Built = 50%, Nat Env = 30%, Engineering = 20%
  Built = 20%, Nat Env = 70%, Engineering = 10%
Or by adjusting combined avoidance and opportunities
  Avoidance = 50%, Opportunities = 50%
  Avoidance = 80%, Opportunities = 20%
Route Examples

## Slide 40: Public Involvement
GeoRoute Selection Model
Model works but has lots of moving parts and can be confusing to an audience
Need to simplify interface
Solution
  Export model to Python
  Develop ArcMap extension using C#
  Extension hooks in to Python

## Slide 41: Conclusion
GeoRoute Selection Model
Model allows PSE to easily compare alternate routes
Model is transparent and reproducible
Data is from authoritative sources and defensible
Solution allows for public input and allows public to see the results immediately

## Slide 42: Questions?
GeoRoute Selection Model
Gene Lohrmeyer
GeoEngineers
glohrmeyer@geoengineers.com
425-861-6000