Chem E 260

HW #9

C&B: 9.91, 9.94, 9.102E , 9.103   and   10.15E, 10.17, 10.23 ,10.34

9-91 A simple Brayton cycle with air as the working fluid has a pressure ratio of 8. The air temperature at the turbine exit, the net work output, and the thermal efficiency are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The air-standard assumptions are applicable. 3 Kinetic and potential energy changes are negligible. 4 Air is an ideal gas with variable specific heats.

Properties The properties of air are given in Table A-17.

Analysis (a) Noting that process 1-2s is isentropic,

Thus,

T4  =  770.1 K

(b)

(c)

9-94 A simple ideal Brayton cycle with air as the working fluid operates between the specified temperature and pressure limits. The net work and the thermal efficiency are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The air-standard assumptions are applicable. 3 Kinetic and potential energy changes are negligible. 4 Air is an ideal gas with constant specific heats.

Properties The properties of air at room temperature are cp  = 1.005 kJ/kg·K  and  k = 1.4  (Table A-2a).

Analysis  Using the isentropic relations for an ideal gas,

Similarly,

Applying the first law to the constant-pressure heat addition process 2-3 produces

Similarly,

The net work production is then

and the thermal efficiency of this cycle is

9-102E A simple ideal Brayton cycle with argon as the working fluid operates between the specified temperature and pressure limits. The rate of heat addition, the power produced, and the thermal efficiency are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Kinetic and potential energy changes are negligible. 3 Argon is an ideal gas with constant specific heats.

Properties The properties of argon at room temperature are R = 0.2686 psia(ft3/lbm·R (Table A-1E), cp = 0.1253 Btu/lbm·R  and  k = 1.667  (Table A-2Ea).

Analysis  At the compressor inlet,

According to the isentropic process expressions for an ideal gas,

Applying the first law to the constant-pressure heat addition process 2-3 gives

The net power output is

The thermal efficiency of this cycle is then

9-103 An aircraft engine operates as a simple ideal Brayton cycle with air as the working fluid. The pressure ratio and the rate of heat input are given. The net power and the thermal efficiency are to be determined.

Assumptions 1 Steady operating conditions exist. 2 The air-standard assumptions are applicable. 3 Kinetic and potential energy changes are negligible. 4 Air is an ideal gas with constant specific heats.

Properties The properties of air at room temperature are cp  = 1.005 kJ/kg·K  and  k = 1.4  (Table A-2a).

Analysis  For the isentropic compression process,

The heat addition is

Applying the first law to the heat addition process,

The temperature at the exit of the turbine is

Applying the first law to the adiabatic turbine and the compressor produce

The net power produced by the engine is then

Finally the thermal efficiency is

10-15E A simple ideal Rankine cycle with water as the working fluid operates between the specified pressure limits. The rates of heat addition and rejection, and the thermal efficiency of the cycle are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Kinetic and potential energy changes are negligible.

Analysis  From the steam tables (Tables A-4E, A-5E, and A-6E),

Knowing the power output from the turbine the mass flow rate of steam in the cycle is determined from

The rates of heat addition and rejection are

and the thermal efficiency of the cycle is

10-17 A simple ideal Rankine cycle with water as the working fluid operates between the specified pressure limits. The power produced by the turbine and consumed by the pump are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Kinetic and potential energy changes are negligible.

Analysis  From the steam tables (Tables A-4, A-5, and A-6),

The power produced by the turbine and consumed by the pump are

10-23 A 300-MW coal-fired steam power plant operates on a simple ideal Rankine cycle between the specified pressure limits. The overall plant efficiency and the required rate of the coal supply are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Kinetic and potential energy changes are negligible.

Analysis (a)  From the steam tables (Tables A-4, A-5, and A-6),

The thermal efficiency is determined from

and

Thus,

(b)  Then the required rate of coal supply becomes

and

10-34 A steam power plant that operates on the ideal reheat Rankine cycle is considered. The turbine work output and the thermal efficiency of the cycle are to be determined.

Assumptions 1 Steady operating conditions exist. 2 Kinetic and potential energy changes are negligible.

Analysis  From the steam tables (Tables A-4, A-5, and A-6),

The turbine work output and the thermal efficiency are determined from

and

Thus,

# Text boxes

2

3

1

6 psia

qout

qin

4

500 psia

s

### T

qin

qout

20 kPa

1

3

2

4

4 MPa

s

### T

Qin

Qout

25 kPa

1

3

2

4

5 MPa

s

### T

·

·

1

5

2

6

s

## T

3

4

8 MPa

20 kPa

s

T

1

2s

4s

3

qin

qout

1160 K

310 K

2

4

s

T

1

2

4

3

qin

qout

1000 K

300 K

s

T

1

2

4

3

qin

qout

1660 R

540 R

s

T

1

2

4

3

qin

qout

273 K