Key questions for biodiesel production:

# Feed Stream

- What are your sources of raw material?  How much do you expect to obtain (percentage of existing supply or all of it)?

- What was the raw material being used for before you obtained it (environmental report consideration)?

- What is the purity of the raw material?

- What is the composition of your raw material?

- Do you have any physical properties for your raw material?

- Is there any pre-processing required for your raw material (oil production from seeds, purifying the waste cooking oil, filtering either source)?

- Is your plant capacity based on the amount of raw material you can obtain or is it based on an amount you want to produce?

# Product Amount

- How much fuel does your audience need?  Can you sell a B100 or does it need to be some form of a blend?  Can you supply the entire demand with a blend?

- Are you including any extra capacity in your plant for an increase in raw material supply or demand?

- Is your production levels dependant upon the season or is it consistent year round?  Are there storage concerns for your product?

# Reactor

- What catalyst did your group choose?  Why did you choose it?

- What reaction temperatures are you choosing and why?  What reaction pressures are you choosing and why?

- What residence time is required for your reactor?  What is the rate of reaction for the system you have selected?

- What type of catalyst did you choose KOH or NaOH or H2SO4 etc.?

- What alcohol are you choosing?  And why?

# Product Purity

- What purity of glycerol do you think you are going to produce (crude or purified)?

- What purity levels are required for your glycerol product?

- What can you do with the salt by-product?  Is it a waste stream, a product stream, a recyclable stream?

- What purity of biodiesel do you need to pass the ASTM standards?

- What are the main impurities in all of the product streams (including the recycled alcohol stream)?

- How will you purify your products?  Is liquid-liquid settling enough?  Is distillation necessary?

Process Design

- What residence time is required for any liquid-liquid settling?

- Is simulation necessary?  What thermodynamic method is appropriate?  How will you verify the results of your simulation efforts?

- What is the most expensive piece of equipment?  Can the cost associated with this piece be reduced?

- Are there opportunities for heat integration in the process?

# Safety

- Are there toxicity or safety concerns with biodiesel?

# Business

- Are there any government subsidies for producing biodiesel?  Hint hint…