## Slide 1
ESS 454 Hydrogeology
Module 4
Flow to Wells
Preliminaries, Radial Flow and Well Function
Non-dimensional Variables, Theis “Type” curve, and Cooper-Jacob Analysis
Aquifer boundaries, Recharge, Thiem equation
Other “Type” curves
Well Testing
Last Comments
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2
Wells:
Intersection of Society and Groundwater
Fluxin- Fluxout= DStorage
Removing water from wells MUST change natural discharge or recharge or change amount stored
Consequences are inevitable
It is the role of the Hydrogeologist to evaluate the nature of the consequences and to quantify the magnitude of effects
Hydrologic Balance in absence of wells:

## Slide 3
Road Map
Math:
plethora of equations
All solutions to the diffusion equation
  Given various geometries and initial/final conditions
Need an entire course devoted to “Wells and Well Testing”
1. Understand the basic principles
2. Apply a small number of well testing methods
Understand natural and induced flow in the aquifer
Determine aquifer properties
  T and S
Determine aquifer geometry:
  How far out does the aquifer continue,
  how much total water is available?
Evaluate “Sustainability” issues
  Determine whether the aquifer is adequately “recharged” or has enough “storage” to support proposed pumping
  Determine the change in natural discharge/recharge caused by pumping
Goal here:
A Hydrogeologist needs to:

## Slide 4: Module Four Outline
Flow to Wells
  Qualitative behavior
  Radial coordinates
  Theis non-equilibrium solution
  Aquifer boundaries and recharge
  Steady-state flow (Thiem Equation)
“Type” curves and Dimensionless variables
Well testing
  Pump testing
  Slug testing

## Slide 5: Concepts and Vocabulary
Radial flow, Steady-state flow, transient flow, non-equilibrium
Cone of Depression
Diffusion/Darcy Eqns. in radial coordinates
  Theis equation, well function
  Theim equation
Dimensionless variables
Forward vs Inverse Problem
Theis Matching curves
Jacob-Cooper method
Specific Capacity
Slug tests
    Log h vs t
      Hvorslev falling head method
    H/H0 vs log t
      Cooper-Bredehoeft-Papadopulos method
Interference, hydrologic boundaries
Borehole storage
  Skin effects
  Dimensionality
  Ambient flow, flow logging, packer testing

## Slide 6: Module Learning Goals
Master new vocabulary
Understand concepts of “non-equilibrium flow”, ”steady-state flow” and “transient flow” and the geologic conditions that control flow
Recognize the diffusion equation and Darcy’s Law in axial coordinates
Understand (qualitatively and quantitatively) how water is produced from an aquifer to the well for both confined and unconfined aquifers
Understand how the Theis equation was derived and be able to use the well function to calculate drawdown as a function of time and distance
Be able to use non-dimensional variables to characterize the behavior of flow from wells
Be able to identify when the Thiem equation is appropriate and use it in quantitative calculations
Be able to use Theis and Jacob-Cooper methods to determine aquifer transmissivity and storativity
Be able to describe how draw-down curves are impacted by aquifer properties or recharge/barrier boundaries and quantitatively estimate the size of an aquifer
Understand how aquifer properties are determined in slug tests and be able to undertake quantitative analysis of Hvorslev and Cooper-Bredehoeft-Papadopulos tests.
Be able to describe what controls flow from wells starting at early time and extending to long time intervals
Be able to describe quantitatively how drawdown behaves if nearby wells have overlapping cones of depression
Understand the limits to what has been developed in this module

## Slide 7: Learning Goals- This Video
Understand the role of a hydrogeologist in evaluating groundwater resources
Be able to apply the diffusion equation in radial coordinates
Understand (qualitatively and quantitatively) how water is produced from a confined aquifer to the well
Understand the assumptions associated with derivation of the Theis equation
Be able to use the well function to calculate drawdown as a function of time and distance

## Slide 8: Important Note
Will be using many plots to understand flow to wells
  Some are linear x and linear y
  Some are log(y) vs log(x)
  Some are log(y) vs linear x
  Some are linear y vs log(x)
Make a note to yourself to pay attention to these differences!!

## Slide 9
Potentiometric surface
Assumptions
Aquifer bounded on bottom, horizontal and infinite, isotropic and homogeneous
Initially horizontal potentiometric surface, all change due to pumping
Fully penetrating and screened wells of infinitesimal radius
100% efficient – drawdown in well bore is equal to drawdown in aquifer
Radial horizontal Darcy flow with constant viscosity and density
Confined Aquifer
Pump well
Observation Wells
Radial flow
surface
Draw-down
Cone of Depression
Assumptions Required for Derivations

## Slide 10: Equations in axial coordinates
b
r
Cartesian Coordinates: x, y, z
Axial Coordinates: r, q, z
No vertical flow
Same flow at all angles q
Flow only outward or inward
Flow size depends only on r
Will use Radial flow:
For a cylinder of radius
r and height b :
r
q
z
Flow through surface of area 2prb

## Slide 11
Diffusion Equation:
Darcy’s Law:
Equations in axial coordinates
Leakage:
Water infiltrating through confining layer with properties K’ and b’ and no storage.
Need to write in axial coordinates with no q or z dependences
Equation to solve for flow to well
Area of cylinder

## Slide 12
Flow to Well in Confined Aquifer with no Leakage
Confined Aquifer
surface
Radial flow
ho: Initial potentiometric surface
Pump at constant flow rate of Q
ho
h(r,t)
r
Wanted: ho-h
Drawdown as function of distance and time
Drawdown must increase to maintain gradient
Gradient needed to induce flow

## Slide 13: Theis Equation
His solution (in 1935) to Diffusion equation for radial flow to well subject to appropriate boundary conditions and initial condition:
for all r at t=0
for all time at r=infinity
Story: Charles Theis went to his mathematician friend C. I. Lubin who gave him the solution to this problem but then refused to be a co-author on the paper because Lubin thought his contribution was trivial. Similar problems in heat flow had been solved in the 19th Century by Fourier and were given by Carlslaw in 1921
No analytic solution
Important step: use a non-dimensional variable that includes both r and t
For u=1, this was the definition of characteristic time and length
Solutions to the diffusion equation depend only on the ratio of r2 to t!
W(u) is the “Well Function”

## Slide 14
For u<1
Theis Equation
Need values of W for different values of the dimensionless variable u
Get from Appendix 1 of Fetter
  u is given to 1 significant figure – may need to interpolate
Calculate “numerically”
  Matlab® command is W=quad(@(x)exp(-x)/x, u,10);
Use a series expansion
  Any function can over some range be represented by the sum of polynomial terms

## Slide 15: Well Function
u | W
10-10 | 22.45
10-9 | 20.15
10-8 | 17.84
10-7 | 15.54
10-6 | 13.24
10-5 | 10.94
10-4 | 8.63
10-3 | 6.33
10-2 | 4.04
10-1 | 1.82
100 | 0.22
101 | <10-5
As r increases, u increases and W gets smaller
Less drawdown farther from well
As time increases, u decreases and W gets bigger
More drawdown the longer water is pumped
Units of length
dimensionless
For a fixed time:
At any distance
Non-equilibrium: continually increasing drawdown
dimensionless
11 orders of magnitude!!

## Slide 16
Well Function
How much drawdown at well screen (r=0.5’) after 24 hours?
How much drawdown 100’ away after 24 hours?
u= (S/4T)x(r2/t)
u=2.5x10-7(r2/t)
Dh (ft)
6.2x10-8
16.0
2.5x10-3
5.4
Aquifer with:
T=103 ft2/day
S = 10-3
T/S=106 ft2/day
Examples
Pumping rate:
Q=0.15 cfs
Q/4pT ~1 foot
Well diameter 1’
Use English units: feet and days
How much drawdown 157’ away after 24 hours?
How much drawdown 500’ away after 10 days?
4.5
6.3x10-3
4.5
6.3x10-3
Same drawdown for different times and distances

## Slide 17
After 1 Day of Pumping
Well Function
Continues to go down
Notice similar shape for time and distance dependence
Notice decreasing curvature with distance and time
Cone of Depression
After 30 Days of Pumping
After 1000 Days of Pumping

## Slide 18
The End: Preliminaries, Axial coordinate, and Well Function
Coming up “Type” matching Curves