## Slide 1
ESS 454 Hydrogeology
Module 2
Properties of Materials
Basic Physics
Darcy’s Law
Characteristics of Aquifers
Elasticity and Storage
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2: Energy
Measured relative to a “datum”
  Difference rather than “absolute value” is important
“additive” and “conserved”
“extensive” (scales with size)
  Units of J/kg or J/m3 or J/N (N=kg*g)
Potential, Kinetic, Thermal, Chemical

## Slide 3
8
6
7
7
7
7
4
5
9
Forms “scalar field”
Surface of constant energy is an “equipotential” surface
Energy

## Slide 4: Force
Gradient (derivative in x, y, and z) of Energy
  Vector
Units: mass*length/time2
Energy increases in gradient direction
  Force “points” in opposite direction
x
E
1
2
Force in –x direction

## Slide 5: Pressure
Force per unit area (N/m2 = Pa)
Gravitational force = r*g (force on a volume)
  g=9.8 m/s2 r is density (kg/m3)
P = r*g *h h is height of column
  Note DP = r*g * Dh (for fluid of constant density)

## Slide 6
  Water density is approximately 1000 kg/m3
  Gravitational acceleration is 9.81 m/s2
  P = r*g *h
  = 1000 kg/m3 * 9.81 m/s2* 100 m
  = 0.981 * 106 Pa
  ~ 1 MPa per 100 m of water
Example: column of water 100 m high

## Slide 7: Groundwater Energy scale
h
Use extensive unit: energy per unit weight:
  J/N = kg m/s2 m/kg s2/m
  Energy can be expressed as a height
    Measure from some elevation. Doesn’t matter as long as we all agree to use the same datum
  “Head” measured as height in an open tube (piezometer)
  Note: change in Head is Dh
  = meters!
  Dh

## Slide 8: Hydraulic Head
Head is a measure of energy
  Two forms of groundwater energy:
    Elevation head
      Height above datum
    Pressure head
      height of water which would create a certain pressure
Energy is scalar and additive
  Just add various contributions

## Slide 9
datum
Commonly: MSL
Surface
1 m
100 m
Energy
Elevation head
+ Pressure head
= Total head
Energy (Head) Example
101 m
0 m
101 m
1 m
100 m
101 m
51 m
50 m
101 m
?
?
?
piezometer
70 m

## Slide 10: The End – Basic Physics
Continue – Darcy’s Law