## Slide 1
ESS 454 Hydrogeology
Module 3
Principles of Groundwater Flow
Point water Head, Validity of Darcy’s Law
Diffusion Equation
Flow in Unconfined Aquifers & Refraction of Flow lines
Flownets
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2
Outline and Learning Goals
Understand how Darcy’s Law and conservation of water leads to the “diffusion equation”
  Solution of this equation gives flow direction and magnitude
Be able to quantitatively determine characteristic lengths or times based on “scaling” of the diffusion equation
Be aware of the range of diffusivities for various rock types

## Slide 3: Is it “Steady-state”?
“Steady-State” :
  Hydraulic heads at all locations are invariant (do not change with time)
“Time-Dependent”
  Hydraulic head in at least one location is changing

## Slide 4
Key idea - Diffusion Equation gives:
    Distribution of hydraulic heads in space and variation of the direction of flow of water
    Scaling between “size” of system and the rate of change of flow with time
The Diffusion Equation:

## Slide 5
dx
dy
dz
qin
qout
Consider box with sides dx, dy, and dz
Water flows in one side and out the other
Flow out is given by the approximation:
qout = qin + dq/dx dx
Hydrologic equation: change in storage = difference between flow in and flow out
=
Since
T=Kdz
h = T/S
Diffusion Equation
h is called Diffusivity
Horizontal area
Vertical area

## Slide 6: Diffusion Equation
Applies if (1) flux is proportional to gradient
(2) water is conserved
Derived formula for 1-D flow. With just a little more algebra effort, the 3-D version is
anisotropy just makes the algebra more complicated
This can be written in calculus notation as:
Diffusion equation is ubiquitous. Applies to electrical flow, heat flow, chemical dispersion, ….

## Slide 7: Diffusion Equation
Partial Differential Equation
Needed to solve: (1) Initial Conditions
(if time dependent)
(2) Boundary Conditions
If flow is “steady-state” then left side is zero:
This is called LaPlace’s Equation
These equations give us the ability to determine the time dependence and the 3-D pattern of groundwater flow
But even without solving the equation, both the time dependence and the pattern of groundwater flow can be estimated

## Slide 8: Ranges of Storativity and Diffusivity
For soils and unconsolidated materials, the skeleton compressibility dominates fluid compressibility
Fractures especially have very small storage and potentially very high T, hence fractured rocks have very high diffusivities compared with non-fractured rocks

## Slide 9
Diffusion Equation
Time Dependence
Write Diffusion
Equation Units:
t
l
Replace units with “Characteristic” values
l 2 = h t
4
Geometric term
This provides a way to estimate the time it takes if you know the length or the distance associated with an interval of time

## Slide 10
Diffusion Equation
Time Dependence
Examples:
(1) Water is pumped from a production well. How long will it be before the water level begins to drop at other wells?
Distance (m) Time (s)
10
100
1000
For sand aquifer: h=0.1 m2/s
250
25,000
2,500,000
4 minutes
7 hours
1 month
(2) After one year how far out will wells begin to see an effect of the pumping well?

## Slide 11
Flow Equations
Solutions to the Diffusion Equation (time dependent flow) or LaPlace’s Equation (steady-state flow) give values of the hydraulic head.
Flow direction and magnitude is calculated from Darcy’s Law:
h=10
h=9
h=8
h=7
100
For Isotropic aquifer, flow is perpendicular to surfaces of constant head
“grad h” is 1/100 = 0.01
Flow direction is horizontal to right
q
Magnitude (size) is K*0.01
Plot equipotential surfaces

## Slide 12
Flow Equations
Solutions to the Diffusion Equation (time dependent flow) or LaPlace’s Equation (steady-state flow) give values of the hydraulic head.
Flow direction and magnitude is calculated from Darcy’s Law:
h=10
100
For Isotropic aquifer, flow is perpendicular to surfaces of constant head
“grad h” is 1/100 = 0.01
Flow direction is coming up from left
q
Magnitude (size) is K*0.01
h=9
h=8
h=7

## Slide 13
The End: Diffusion Equation
Coming up: Flow in Unconfined Aquifers