## Slide 1
ESS 454 Hydrogeology
Module 2
Properties of Materials
Basic Physics
Darcy’s Law
Characteristics of Aquifers
Elasticity and Storage
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2: Learning Objectives Darcy’s Law
Be able to use Darcy’s Law to calculate water fluxes and to quantify permeameter properties
Be able to describe and distinguish, and use in quantitative calculations: hydraulic conductivity, permeability, and hydraulic head (total, elevation, pressure)

## Slide 3: Darcy’s Experiment and Law
Pressure Gauge
Pressure Gauge
Basin to collect a volume of water
Tube of length “L” and area “A” filled with soil
Flux Q is volume of flow per unit time
  Cubic feet per second (cfs), liters per minute (l/min), etc
Q ∝ ∆P 1/L A
Water pumped in
Water flows out

## Slide 4: Hydraulic Conductivity
Define K as Hydraulic Conductivity and replace ∆P with ∆h
Q = K A ∆h/L
Generalize using calculus:
  Q = -K A dh/dl
Specific discharge
  q = Q/A = - K dh/dl
  dh/dl is dimensionless
  K and q have units of velocity
    Specific discharge is called “Darcian Velocity”
Minus sign is important – more later
∆P=r g ∆h
Instead of Q ∝ ∆P 1/L A

## Slide 5: More Generalizations Darcy’s Law
Specific discharge is a vector – it has a size (magnitude) and a direction
dh/dl is the derivative of hydraulic head with length
This is a spatial gradient of the energy of the water
Replace with gradient (dh/dx, dh/dy, dh/dz)
Remember that so is a force acting on water
The minus sign is important to move water in the correct direction
K (hydraulic conductivity) can depend on direction of flow. The two arrows indicate this complication

## Slide 6: Permeameter Device to measure hydraulic conductivity of materials
Discuss Steady-State examples (Falling Head discussed in book)
Height of input
Dh
L
Area A
direction of flow
Dh
Height of output
Direction of flow

## Slide 7: Permeability
Hydraulic Conductivity depends on properties of both fluid and medium:
  Larger spaces for fluid to flow through: K up
  Larger specific weight (g=rg) of fluid: K up
  Larger viscosity (m) of fluid: K down
K is equal to product of contributions:
K = (C*d2) * (g/m)
Intrinsic Permeability (k or Ki)
Property of Medium
Property of Fluid

## Slide 8
Ki = C d2
  C is a “shape factor”
  d is the effective “size” of the passage for the fluid
  Permeability has units of area
Petroleum Engineers defined Darcy unit:
1 Darcy = 1 cP * 1 cm3/s / 1 cm2 / (1 atm / 1 cm)
= 9.87x10-9 cm2
Permeability depends only on the
geometry of passages within the matrix

## Slide 9: More on Hydraulic Conductivity
Viscosity and density depend on temperature:
  for T up, m goes down (large effect) and r goes down (smaller effect) -> K goes up
  Pure water at 15.6°C and 1 atm is standard
ft/day is common (USGS) unit for K and for q

## Slide 10: Properties of Sediments
 | K (cm/s) | Ki (Darcys)
Clay | 10-9 – 10-6 | 10-6 – 10-3
Silt | 10-6 – 10-4 | 10-3 – 10-1
Fine Sand | 10-5 – 10-3 | 10-2 – 1
Well sorted Sand | 10-3 – 10-1 | 1 – 100
Well sorted gravel | 10-2 – 1 | 10 – 1000
Variation of 9 orders of magnitude!
3x10-6 – 3x10-3 ft/day
3x10-3 – 3x10-1 ft/day
0.03 – 3 ft/day
3 – 300 ft/day
0.3 – 3000 ft/day

## Slide 11
datum
1
2
3
4
5
6
Elevation (m)
Given:
Q=6 liters/minute
= 0.1 liters/s
= 10-4 m3/s
A= 0.05 m2
L=1m
4. What is the hydraulic conductivity of material in this permeameter?
a
b
c
d
What are the elevation heads, pressure heads and total heads at points a, b, c, and d?
What is the head difference between the inlet and outlet?
Which way does water flow?

## Slide 12: The End – Darcy’s Law
Continue – Characteristics of Aquifers