## Slide 1
ESS 454 Hydrogeology
Module 4
Flow to Wells
Preliminaries, Radial Flow and Well Function
Non-dimensional Variables, Theis “Type” curve, and Cooper-Jacob Analysis
Aquifer boundaries, Recharge, Thiem equation
Other “Type” curves
Well Testing
Last Comments
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2
Learning Objectives
Recognize causes for departure of well drawdown data from the Theis “non-equilibrium” formula
Be able to explain why a pressure head is necessary to recover water from a confined aquifer
Be able to explain how recharge is enhanced by pumping
Be able to qualitatively show how drawdown vs time deviates from Theis curves in the case of leakage, recharge and barrier boundaries
Be able to use diffusion time scaling to estimate the distance to an aquifer boundary
Understand how to use the Thiem equation to determine T for a confined aquifer or K for an unconfined aquifer
Understand what Specific Capacity is and how to determine it.

## Slide 3
When Theis Assumptions Fail
Total head becomes equal to the elevation head
  To pump, a confined aquifer must have pressure head
  Cannot pump confined aquifer below elevation head
  Pumping rate has to decrease
Aquifer ends at some distance from well
  Water cannot continue to flow in from farther away
  Drawdown has to increase faster and/or pumping rate has to decrease

## Slide 4
When Theis Assumptions Fail
straw
Air pressure in unconfined aquifer pushes water up well when pressure is reduced in borehole
If aquifer is confined, and pressure in borehole is zero, no water can move up borehole
“Negative” pressure does not work to produce water in a confined aquifer
cap
Reduce pressure by “sucking”
No amount of “sucking” will work

## Slide 5
When Theis Assumptions Fail
Leakage through confining layer provides recharge
  Decrease in aquifer head causes increase in Dh across aquitard
    Pumping enhances recharge
    When cone of depression is sufficiently large, recharge equals pumping rate
Cone of depression extends out to a fixed head source
  Water flows from source to well

## Slide 6
Flow to well in Confined Aquifer with leakage
Aquifer above Aquitard
surface
Confined Aquifer
ho: Initial potentiometric surface
Dh
Increased flow through aquitard
As cone of depression expands, at some point recharge through the aquitard may balance flow into well
larger area -> more recharge
larger Dh -> more recharge

## Slide 7
surface
Confined Aquifer
ho: Initial potentiometric surface
Flow to Well in Confined Aquifer with Recharge Boundary
Lake
Gradient from fixed head to well

## Slide 8
Flow to Well –Transition to Steady State Behavior
Non-equilibrium
Steady-state
t
Both leakage and recharge boundary give steady-state behavior after some time interval of pumping, t
Hydraulic head stabilizes at a constant value
The size of the steady-state cone of depression or the distance to the recharge boundary can be estimated

## Slide 9: Steady-State Flow Thiem Equation – Confined Aquifer
Confined Aquifer
surface
r2
h2
r1
h1
When hydraulic head does not change with time
Darcy’s Law in radial coordinates
Rearrange
Integrate both sides
Result
Determine T from drawdown at two distances
In Steady-state – no dependence on S

## Slide 10: Steady-State Flow Thiem Equation – Unconfined Aquifer
surface
r2
b2
r1
b1
When hydraulic head does not change with time
Darcy’s Law in radial coordinates
Rearrange
Integrate both sides
Result
Determine K from drawdown at two distances
In Steady-state – no dependence on S

## Slide 11
  Specific Capacity (driller’s term)
1. Pump well for at least several hours – likely not in steady-state
2. Record rate (Q) and maximum drawdown at well head (Dh)
3. Specific Capacity = Q/Dh
This is often approximately equal to the Transmissivity
Why??
Specific Capacity
??

## Slide 12
Example: My Well
Typical glaciofluvial geology
Driller’s log available online through Washington State Department of Ecology
Till to 23 ft
Clay-rich sand to 65’
Sand and gravel to 68’
6” bore
Screened for last 5’
Static head is 15’ below surface
Pumped at 21 gallons/minute for 2 hours
Drawdown of 8’
Specific capacity of:
=4.1x103/8=500 ft2/day
Q=21*.134*60*24
= 4.1x103 ft3/day
K is about 100 ft/day
(typical “good” sand/gravel value)

## Slide 13
The End: Breakdown of Theis assumptions and steady-state behavior
Coming up: Other “Type” curves