## Slide 1
ESS 454 Hydrogeology
Module 3
Principles of Groundwater Flow
Point water Head, Validity of Darcy’s Law
Diffusion Equation
Flow in Unconfined Aquifers & Refraction of Flow lines
Flownets
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2
Know the appropriate boundary conditions of head and flux for various types of boundaries
Be able to qualitatively and quantitatively estimate equipotential lines, flux lines, and discharge/recharge rates using flownets
Outline and Learning Goals

## Slide 3: 2-D Reconstructions (Flownets)
Graphical solution to LaPlace’s equation
Semi quantitative
Important in building “intuitive” understanding of groundwater flow

## Slide 4: Major Assumptions
The situation is 2-D
Aquifer is
  Homogeneous
  Isotropic
  Saturated
Steady-state, incompressible laminar flow
Known boundary conditions
(rule of thumb L= 5xW)

## Slide 5: Boundary Types
No Flow
  Flow lines are parallel to boundary
  Equipotential lines are perpendicular
Constant Head
  Flow lines are perpendicular
  Adjacent equipotential lines are parallel
Water table (Known head)
  No recharge: flow is parallel
  With recharge flow is oblique down
Standing water

## Slide 6: Overall Plan
Plot boundaries to scale
Sketch equipotential line (stubs) at boundaries
Near boundaries draw flow perpendicular to equipotential lines
Extend flow lines to connect recharge to discharge regions
Connect equipotential lines to insure that they are perpendicular to flow lines everywhere
important!!!

## Slide 7: The process is iterative
Draw boundaries
Identify boundary conditions and sketch local flow
Pencil in trial equipotential and flow lines
Erase and adjust lines until a satisfactory net is achieved
  Flow lines and equipotential lines should define nearly uniform equi-dimensional “squares”
  Must be 90° angle between all flow lines and intersecting equipotential lines
Calculate flow as q’= K h p/f
  Where q’ is discharge per width
  p is number of flow tubes
  f is number of squares along flow tube
  h is total head difference

## Slide 8: Example 1
Impermeable boundary
Impermeable boundary
h=40’
h=20’
Top and bottom are “No flow”
Flow is parallel and equipotential lines are perpendicular
Sides are “Constant Head”
Flow is perpendicular and equipotential lines are parallel
Flow Tube
q’ is volume discharge per unit width
K is hydraulic Conductivity
p is number of flow tubes
h is total head loss
f is number of squares along flow tubes
Semi-quantitative analysis
4
20’
9
q’=Kph/f

## Slide 9: Example 2
8’
0 ft
No flow
Constant head
Constant head
No flow
No flow
No flow
Any 2-D flow situation can be estimated by constructing a Flownet
Try it yourself for another geometry
h=10
h=1
Needs adjusting: not 90°

## Slide 10
The End of Module 3
Should have
a conceptual grasp of how water flows in aquifers
  a. Flow perpendicular to equipotential lines
  b. Boundary conditions
An understanding of the equations that control flow
  Diffusion Equation
  LaPlace’s Equation
Coming up: Flow of water to wells