## Slide 1
ESS 454 Hydrogeology
Module 4
Flow to Wells
Preliminaries, Radial Flow and Well Function
Non-dimensional Variables, Theis “Type” curve, and Cooper-Jacob Analysis
Aquifer boundaries, Recharge, Thiem equation
Other “Type” curves
Well Testing
Last Comments
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 2
Learning Objectives
Forward problem: Understand how to use the Hantush-Jacob formula to predict properties of a confined aquifer with leakage
Inverse problem: Understand how to use Type curves for a leaky confined aquifer to determine T, S, and B
Understand how water flows to a well in an unconfined aquifer
  Changes in the nature of flow with time
  How to use Type curves

## Slide 3
Other Type-Curves
Given without Derivations
Leaky Confined Aquifer
  Hantush-Jacob Formula
  Appendix 3 of Fetter
“Type Curves” to determine T, S, and r/B
Drawdown reaches “steady-state” when recharge balances flow
Larger r/B -> smaller steady-state drawdown
Same curve matching exercise as with Theis Type-curves
New dimensionless number
Large K’ makes r/B large

## Slide 4
Other Type-curves –
Given without Derivations
2. Unconfined Aquifer
  Neuman Formula
  Appendix 6 of Fetter
Similar to Theis but more complicated:
Initial flow from elastic storage - S
Late time flow from gravity draining – Sy
  Remember: Sy>>S
Vertical and horizontal flow –
  Kv may differ from Kh
Three non-dimensional variables
Initial flow from Storativity
Later flow from gravity draining
Difference between vertical and horizontal conductivity is important

## Slide 5
Flow in Unconfined Aquifer
surface
Flow from elastic storage
Vertical flow (gravity draining)
Horizontal flow induced by gradient in head
1. Elastic Storage
Time order
Flow from gravity draining and horizontal head gradient
Start Pumping

## Slide 6
Other Type-curves –
Given without Derivations
Two-step curve matching:
Fit early time data to A-type curves
Fit late time data to B-type curves
2. Unconfined Aquifer
  Neuman Formula
  Appendix 6 of Fetter
Depends on Elastic Storage S
Depends on Specific Yield Sy
Theis curve using Elastic Storage
Theis curve using Specific Yield
Transition depends on ratio r2Kv/(Khb2)
Sy=104*S
Sy=103*S

## Slide 7
The End: Other Type Curves
Coming up: Well Testing