## Slide 1
ESS 454 Hydrogeology
Instructor: Michael Brown
brown@ess.washington.edu
Module 5
Regional Groundwater Flow
Regional and Local Flow
Vectors, Matrixes, and Coordinate transformation
Anisotropic Hydraulic Conductivity
Groundwater interactions with surface water

## Slide 2: Module 5 Concepts
Recharge and discharge regions
Local and regional flow systems
Stream lines and equipotential lines
Flow system boundary, stagnation point
Effects due to
  Buried lenses
  Layered hydraulic conductivity differences
Anisotropy => tensor properties of K and Darcy’s Law
Dynamic equilibrium
Fossil water/connate water/juvenile water/magmatic water
Karst terrains
Springs- depression/contact/fault/fracture/sinkhole

## Slide 3: Learning Goals
Master new vocabulary and geologic terms
Be able to construct qualitatively correct flownets for all cross-sectional examples given in Chapter 7
Be able to identify areas of recharge and discharge and to be able to show how hydraulic heads varies with depth.
Understand the concepts of local vs regional flow and be able to identify it in flownets given in chapter 7
Be able to locate and label “flow system boundaries” and “stagnation points” on flownets
Understand qualitatively how anisotropy of hydraulic conductivity impacts flow direction
Be able to undertake quantitative calculation of flow direction and fluxes in anisotropic situations
Be able to give examples that illustrate the principal of “dynamic equilibrium” in groundwater systems
Understand that some groundwater is “non-cyclical”
Understand principals associated with the interaction of groundwater with surface water

## Slide 4: Learning Goals-This Video
Be able to construct qualitatively correct flownets for all cross-sectional examples given in Chapter 7
Be able to identify areas of recharge and discharge and to be able to show how hydraulic heads varies with depth.
Understand the concepts of local vs regional flow and be able to identify it in flownets given in chapter 7
Be able to identify flow system boundaries and stagnation points
Be able to construct flownet with layered conductivity

## Slide 5
Flownet Review
Applicable for 2-D steady-state flow
Graphical solution to LaPlace’s Equation
Identify flow boundary types
  No flow
    Flow parallel to boundary potential lines perpendicular to boundary
  Constant head
    Flow perpendicular, local potential parallel
  Water table
    No recharge – flow parallel, potential perpendicular
    Recharge – flow oblique downward
Construct flow lines and equipotential lines that
  do not cross
  are mutually perpendicular
  match boundary conditions

## Slide 6
Fetter 7.1-2 from M.K. Hubbert 1940
Flownet for isotropic homogeneous aquifer
Flow Divide
flow
Lines close->high flow
Lines far apart-> low flow
Flow divide
Recharge Region
Discharge Region
Discharge Region
Piezometers – measure heads at bottom of holes
Dh
Flow down
Bottom is not shown
Dh
Flow up

## Slide 7
Fetter 7.3 from Toth 1960
Flownet for regional groundwater flow with sloping water table
Sloping water table (High on right side)

## Slide 8
Fetter 7.4A
From Toth 1963
Flownet for basin with 20:1 aspect ratio and sloping water table with undulations
Flow
Flow
Flow
Flow
Flow
Flow
Flow
Flow

## Slide 9
Fetter 7.4B
From Toth 1963
Flownet for basin with 2:1 aspect ratio and sloping water table with undulations

## Slide 10
Figure 7.5 from Toth 1963
Flownets showing effect of undulation amplitude

## Slide 11
Fetter 7.6
Flow System Boundary
Stagnation point
(no local gradient)

## Slide 15
Highest head
Low Conductivity

## Slide 16
Example using MATLAB pdetool

## Slide 17
The End
Coming up: Vectors and Matrixes

## Slide 18
ESS 454 Hydrogeology
Module 5
Regional Groundwater Flow
Regional and Local Flow
Vectors, Matrixes, and Coordinate transformation
Anisotropic Hydraulic Conductivity
Groundwater interactions with surface water
Instructor: Michael Brown
brown@ess.washington.edu

## Slide 19: Learning Objectives
Review of vectors and matrixes
  How to represent vectors
  How to describe their properties
    direction and magnitude
  How to represent a Matrix
  How to multiply a matrix and a vector
How to rotate coordinate systems

## Slide 20
z
x
y
r
rx
rz
ry
Vectors
“size” or “magnitude” is length of r
Often convenient to write r as column

## Slide 21
z
Vector Directions
x
y
North
East
N30E
Given
How do you describe this vector?
7
3
q
-2
Dip angle
7.62
Horizontal length
Dip angle
Description :
To two significant figures
Magnitude is 7.9
Direction is N67E
Dip angle is 15°
I

## Slide 22
Matrix: array of numbers
j is row index
Matrixes
i is column index

## Slide 23
Matrix times a vector
Gives a vector
Multiply a Matrix and a Vector
Result will be a new Vector

## Slide 24
Multiply a Matrix and a Matrix
Result will be new Matrix

## Slide 25
Comment
Matrix and vector multiplication is “easy” but “tedious”
Best to use numerical environment like Mathematica or Matlab
>> m=[1 2 3
4 5 6
7 8 9];
>> n=[11 12 13
14 15 16
17 18 19];
>> m*n
90 96 102
216 231 246
342 366 390
Matlab example:
Enter two matrixes and multiply them together

## Slide 26
Coordinate Rotation
x
y
Why?
x’
y’
q
Call this 3x3 matrix the transformation matrix
It “transforms” coordinates xyz into coordinates x’y’z’
Put this together as matrix multiplies
Geologic structures do not necessarily line up with map coordinates
– need tools to transform from “natural” coordinates of the geology to map coordinates
Convention: q is measured counter-clockwise
Consider x’ to be a vector
q

## Slide 27
Coordinate Rotation
Rotation about the x-axis
Rotation about the y-axis
Use aij as label for transformation matrix
Can make compound rotation (first rotate about x, then rotate about y) by multiplying transformation matrixes together

## Slide 28
Coordinate Rotation
Make substitution: 1==x, 2==y, 3==z
x y z
Old coordinates
New coordinates
x’
y’
z’
x’=[axxx , axyy, axzz]
And similarly for y’ and z’
z=[axzx’,ayzy’,azzz’]
Converting to new coordinates
Going from new back:
Sum of squares of any row or column is 1
And similarly for y and x

## Slide 29
Coordinate Rotation
Example:
E
N
x
y
strike
dip
R=[2x,1y,0z]
q
q=45°
What is the direction of R in map coordinates?
A clock-wise rotation is needed here
N??E

## Slide 30
The End: Review of Vectors and Matrixes and Coordinate rotation
Coming Up: Tensor Representation of Hydraulic Conductivity

## Slide 31
ESS 454 Hydrogeology
Instructor: Michael Brown
brown@ess.washington.edu
Module 5
Regional Groundwater Flow
Regional and Local Flow
Vectors, Matrixes, and Coordinate transformation
Anisotropic Hydraulic Conductivity
Groundwater interactions with surface water

## Slide 32: Learning Objectives
What is a Tensor?
How do Tensors transform with Coordinate systems?
Why is hydraulic conductivity a Tensor?
How can Tensor values of K be determined?
How is Flow calculated for Tensor conductivity?

## Slide 33
Tensors
What are they?
0th rank Tensor is a scalar
1st rank Tensor is a vector (3 components)
2nd rank Tensor is a 3x3 matrix
Mathematical definition: Tensors are objects that obey “certain”
rules for transformation of coordinates
Physical (pragmatic) definition: Tensors describe the directional
properties of physical systems
We will use a 2nd rank tensor (a 3x3 matrix) to describe the directional properties of K, the hydraulic conductivity
Scalar K becomes
a 3x3 matrix of numbers

## Slide 34
Tensors
Transformation Rule:
at is the transpose of a
a is the matrix to change coordinates
Switch matrix elements across the diagonal
1. Do K times at
2. Multiply a and that
product

## Slide 35
Why is K a Tensor?
K often is different in different directions
1. Vertical relative to horizontal
Particles can align under gravity so that the flow path is “easier” in one direction
Vertical flow may be more “tortuous” than horizontal flow
Plate-like (clay) particles
Kv < Kh

## Slide 36
Why is K a Tensor?
2. Fracture direction
Flow is “easy” in direction of fractures
Flow is “hard” between fracture planes
K within plane of fractures is large
K in direction between fractures is small
And many other geologic reasons

## Slide 37
K as Tensor
Look intimidating – But really not so bad
At worst, 6 numbers are needed (Tensor is symmetric – Kxy=Kyx)
Even Better:
There is a coordinate system where K is “diagonal” – with only three independent values

## Slide 38
K as Tensor
Math Theorem: In a particular coordinate system, the conductivity tensor is diagonal. Call this the “Principal Coordinates”
K1 is conductivity in x-direction
K2 is conductivity in y-direction
K3 is conductivity in z-direction
In this coordinate system, there is a simple interpretation of the three non-zero values
Off-diagonal components are generated when coordinates are shifted to non-principal coordinates

## Slide 39
Rotate K about z-axis

## Slide 40
Rotate K about z-axis
And q=45°
If
Rotation about the z-axis “generated” off-diagonal (but symmetric) elements

## Slide 41
General Rules
To determine Tensor K, use the “natural coordinates” of the situation:
(Coordinates aligned with “hard” and “easy” directions of flow)
These will be “Principal Coordinates” where K is diagonal and the three non-zero values can be assigned by “inspection”
Example: flow with planar and parallel fractures:
K in the plane of the fractures (2 directions) will be the
“fracture” conductivity
K perpendicular to the fracture plane will be much smaller
Once you know the “principal coordinate” tensor, simply rotate it to the standard (map-based) coordinate system

## Slide 42
Determining K Example
North
East
Fractures trend N40E
K in fracture direction is 10 ft/day
K perpendicular to fractures is 1 ft/day
What is the tensor representation of K using map coordinates?
N40E
Assume east is x-axis, north is the y-axis and z is up and down

## Slide 43
Now we need to rotate K into the map coordinates
In Natural coordinates
(aligned with the fractures)
The x and z axes are in the fracture plane
East
Thus
Kx is large in fracture plane
and Ky is small across fractures
North
East
North
x
y
Determining K Example

## Slide 44
North
East
We need to rotate our tensor from natural coordinates to map coordinates
The natural coordinate x is in the fracture direction
The map direction x’ (East) is a 50° clockwise rotation from x
Thus to rotate the natural coordinates to map coordinates we need a -50° rotation:
50°
Determining K Example

## Slide 45
Remember the result for a rotation about the z-axis
Substituting in -50° and K1=10, K2=1
Determining K Example
Tensor K in map coordinates

## Slide 46
Darcy’s Law with Tensor Conductivity
Use simple example where the vertical conductivity is smaller than the horizontal conductivity
Kh>Kv

## Slide 47
x
z
Examples
x
z
x
z
45° from x
27° from x
Gradient along principal axis causes flow parallel to axis
Gradient in general direction results in flow that is NOT parallel to gradient

## Slide 48
The End
Coming Up: Groundwater Interactions with Surface Water

## Slide 49
ESS 454 Hydrogeology
Instructor: Michael Brown
brown@ess.washington.edu
Module 5
Regional Groundwater Flow
Regional and Local Flow
Vectors, Matrixes, and Coordinate transformation
Anisotropic Hydraulic Conductivity
Groundwater interactions with surface water

## Slide 50: Learning Objectives
Be able to give examples that illustrate the principal of “dynamic equilibrium” in groundwater systems
Understand that some water is “non-cyclical”
  fossil, connate, magmatic, juvenile
Understand principals associated with the interaction of groundwater with surface water

## Slide 51: “Dynamic equilibrium”
Fluxout = Fluxin +/- change in storage
“Equilibrium” implies steady-state
  Net flow in is balanced by flow out
A system cannot continue to add to or subtract from storage
  Natural systems reach situation where change in storage is zero or nearly zero
  It is in “equilibrium” at that point
However, changes are inherent to natural systems
  Annual precipitation varies
  Amount of groundwater pumping changes
Thus, the “equilibrium state” must shift to match new conditions
  Call this a “Dynamic Equilibrium”

## Slide 52
Non-cyclical water
Fossil water has been locked in rock that is sufficiently impermeable to eliminate flow for a long time
Connate water was trapped in the rock at the time of its formation and resides in pores that are not interconnected
“Juvenile water” is water that is making it’s first appearance at Earth’s surface
  At least four oceans worth of water are still trapped in Earth’s mantle.
  Some of this water finds its way into volcanic systems and is vented at Earth’s surface
“Magmatic water” is water released from volcanic systems ( both “juvenile” and groundwater that is dissolved in the magma)
Not all groundwater is free to cycle through the groundwater-surface water system

## Slide 53
Springs
Aquifer hydraulic head is at local surface level, a path to surface is available, and surface water can flow away
Unconfined water table reaches surface
Local surface low

## Slide 54
Springs
Aquifer hydraulic head is above local surface level, a path to surface is available, and surface water can flow
Lower confining layer and aquifer terminate at a steep slope
Spring water emerges at contact

## Slide 55
Springs
Aquifer hydraulic head is above local surface level, a path to surface is available, and surface water can flow
Fault offsets aquifer and creates barrier boundary

## Slide 56
Springs
Aquifer hydraulic head is above local surface level, a path to surface is available, and surface water can flow
Karst Terrain includes “solution cavities” (frequently aligned with joints and cracks)
“Sinkholes” occur when cavity ceiling collapses

## Slide 57
Springs
Aquifer hydraulic head is above local surface level, a path to surface is available, and surface water can flow
Path to surface may be provided by natural cracks (joints).

## Slide 58
Springs
Aquifer hydraulic head is above local surface level, a path to surface is available, and surface water can flow
“Fracture zone” implies more pervasive jointing due to stress-induced breakage

## Slide 60
Streams, lakes and wetland interactions
Contours give levels of hydraulic head
Wetlands or lakes are found where hydraulic head and surface are at same elevation
Surface water can feed into groundwater or be replenished by ground water
Pay attention to direction of flow
Gradient induced flow to lake
Gradient induced flow from lake

## Slide 61
Streams, lakes and wetland interactions
Lake can gain water from groundwater
Stream has flow from lake
and loses water through a stream
and is gaining flow from groundwater

## Slide 62
Streams, lakes and wetland interactions
Lake gaining from groundwater and from stream flow
Lake losing only from groundwater flow
Streams gaining from groundwater

## Slide 63
Streams, lakes and wetland interactions
Lake gaining from streams and groundwater flow
Lake losing from streams and groundwater flow
All streams gaining from groundwater

## Slide 64
Streams, lakes and wetland interactions
Lake gaining from streams a nd groundwater
Lake losing from stream and groundwater
Lower stream losing to groundwater

## Slide 65
Streams, lakes and wetland interactions
Lake gaining from groundwater and from streams
No surface or groundwater leaving lake

## Slide 66: Module 5 Summary
Master new vocabulary and geologic terms
Be able to construct qualitatively correct flownets for all cross-sectional examples given in Chapter 7
Be able to identify areas of recharge and discharge and to be able to show how hydraulic heads varies with depth.
Understand the concepts of local vs regional flow and be able to identify it in flownets given in chapter 7
Be able to locate and label “flow system boundaries” and “stagnation points” on flownets
Understand qualitatively how anisotropy of hydraulic conductivity impacts flow direction
Be able to undertake quantitative calculation of flow direction and fluxes in anisotropic situations
Be able to give examples that illustrate the principal of “dynamic equilibrium” in groundwater systems
Understand that some groundwater is “non-cyclical”
Understand principals associated with the interaction of groundwater with surface water

## Slide 67
The End: Module 5 - Regional Groundwater Flow
Coming Up: Geologic Occurrences of Groundwater