Chapter 5

Making Choices about Geospatial Database Development

Table 5.1. Spatial Data Construct Types Associated with Data Models

|  | Logical Data Models |
| --- | --- |
| Spatial Data Construct Type | Raster Data Models | Vector Data Models |
|  | Image | Grid | TIN | Shapefile | Coverage | Geodatabase |
| Image cell | X |  |  |  |  | X |
| Grid cell |  | X |  |  |  | X |
| Point |  |  |  | X | X | X |
| Multipoint |  |  |  | X |  | X |
| Node |  |  | X |  |  |  |
| Segment/ Polyline |  |  |  | X | X | X |
| Link |  |  | X |  |  |  |
| Chain / Arc |  |  |  |  | X |  |
| Face |  |  | X |  |  |  |
| Tic |  |  |  |  | X |  |
| Annotation |  |  |  | X | X | X |
| Simple junction |  |  |  |  |  | X |
| simple edge |  |  |  |  |  | X |
| Complex junction |  |  |  |  |  | X |
| Complex edge |  |  |  |  |  | X |
| Section |  |  |  |  | X |  |
| Route |  |  |  |  | X |  |
| Ring |  |  |  | X |  | X |
| Polygon |  |  |  | X | X | X |
| Region |  |  |  |  | X |  |
| Network |  |  |  |  | X | X |

Table 5.2. Spatial, Logical, and Temporal Relationships Underlying Operation Activity

|  | Data models |
| --- | --- |
| Relationship | Image | grid | TIN | Shapefile | coverage | geodatabase |
| Spatial Distance & Geometry | Derived | derived | derived | Derived | derived | derived |
| Spatial Topologic Explicit/implicit | Implicit | implicit | Explicit | Derived | explicit | explicit |
| Connectedness | Implicit | implicit | Explicit | Derived | explicit | explicit |
| Adjacency | Implicit | implicit | Explicit | Derived | explicit | explicit |
| Containment | derived | derived | Explicit | Derived | explicit | explicit |
| Function Logic | derived | derived | Derived | Derived | derived | rules stored |
| Temporal Logic | derived | derived | Derived | Derived | derived | rules stored |

Key:

implicit – stored as part of the geometry, easily derived

explicit – stored within a field, easily processed

derived – information computable, but time consuming

none – cannot be processed from available information

Table 5.3. Data Types

Numeric

Integer – positive or negative whole number, usually 32 bits

Long Integer – positive or negative whole number, usually 64 bits

Real (floating point) – single precision decimal number

Double (floating point) – double precision decision number

Character (text string) – alpha-numeric characters

Binary – numbers stored as 0 or 1 expression

Blob/Image – scanned raster data of usually very large size

Geometry shape (Figure 5.2 are all shapes)

Table 5.4. Geodatabase Database Design Process as Data Modeling

Conceptual Design of a Database Model

Identify the information products or the research question to be addressed

Identify the key thematic layers and feature classes.

Detail all feature class(es)

Group representations into datasets

Logical Design of a Database Model

Define attribute database structure and behavior for feature classes

Define spatial properties of datasets

# Physical Design of a Database Model

Data field specification

Implementation

Populate the database

# Table 5.5. Simplified Value Structure for a Green County Database

| Value | Goals/ Target | Objective | Criterion for Site Suitability from Table 3.2 |
| --- | --- | --- | --- |
| Community financial frugality is important. | Less than 365 meters | Minimizing the elevation leads to lower pumping costs | Elevation measured in meters |
| Community environmental health is important. | Outside the 100 year floodplain | The farther outside (up to a limit) the floodplain the less susceptibility to ecosystem degradation | Floodplain measured as elevation below mean sea level |
| Financial frugality is important. | Lowest engineering costs possible translated as 1000 meters of river. | The closer to the river the less cost to build outflow piping | Within 1000 meter distance of river. |
| Community environmental health is important. | Human health is protected when site is at least 150 meters from property. | The farther from residential property the healthier the residents | Euclidean distance in meters from residential property. |
| Green County landscape aesthetics are important. | At least 150 meters from parks. | The farther from park property the better preservation of park aesthetics | Euclidean distance in meters from parks. |
| Green County has some available property to serve as a location. | On vacant land. | Identify all vacant land parcels as an initial qualifier | Land vacancy. |
| Financial frugality is important. | Within 1000 meters of the wastewater pipe junction. | The closer to an existing wastewater pipe of appropriate diameter the better | Euclidean distance to wastewater pipe junction in meters. |
| Financial frugality is important. | Within 50 meters of a road. | The closer to an existing roadway the better | Euclidean distance to roads in meters. |
| Provide for needs of future residents, businesses, and industry. | At least 150,000 square meters. | Only those vacant land parcels large enough will do | Square meters of parcels. |
| Additional concerns |
| Clean water is needed for a healthy Green County community | Locate site within 1000 meters of large gray water users. | Maximize the availability of gray water | Euclidean distances to large gray water users in meters. |
| Appropriate river flow makes for a healthy river. | River flows within 70-90 thousand cubic feet per second range are most preferred. | Min and max river flow should not fall outside of 20,000 – 110,000 cubic feet per second | River flows cubic feet per second. |
| Healthy fish communities help form a healthy human community. | Minimize the impacts on steelhead trout, no more than 1 trout in 1000 to be impacted. | Maximize the improvement of water quality for all fish | No more than X steelhead trout in X to be impacted. |

Table 5.6. Geographic Information Categories and Data Layer Needs for the Original Green County GIS Project and an Enhanced GIS Project

| Geographic Information Needs (based in part on Table 3.2) original Green County Project + enhanced Green County Project | Geographic Data Layer (based in part on Table 3.2) original Green County GIS Project + enhanced Green County GIS Project |
| --- | --- |
| Basemap Environmental characteristics + Soil characteristics Topography Water courses Land cover/use + Natural hazards Ecologically sensitive areas Infrastructure characteristics + Buildings Transportation Utilities + Other utilities Land designations + Zoning Land administration + Boundaries Land ownership + Boundaries | Coordinate reference system + Layer: Soil series Source: NRCS Map use: display and analysis of soil characteristics Layer: Elevation (DEM) Source: Greenvalley DOT; USGS Map use: display and analysis of topographic terrain Layer: National Hydrographic Dataset Source: Green County; USGS and EPA Map use: display and analysis of surface water flows and water quality Layers: Parcel boundaries Land use + Site address Source: City of Greenvalley + Vegetation/Land cover Source: Multiple agencies (EPA, USGS, BLM, various state agencies) Map use: display and analysis of vegetation land cover Layers: + Geohazards + Floodplain areas + Tsunami-prone areas + Historic wildfires Source: multiple agencies including USGS, US Forest Service, state agencies Map use: display and analysis of natural hazard risk Layers: Wetlands/Lowlands Parks Source: City of Greenvalley + Protected areas + Protected habitats Sources: multiple agencies including USGS, EPA, US Forest Services, GAP-Analysis program, state agencies Map use: display and analysis Layers: + Building footprints Roads Streets Sewer lines Source: City of Greenvalley + Gas and electricity lines + Water lines + Ground water wells + Septic tanks + Landfills Source: various local land use and planning management agencies, DOT, local utility providers Map use: display and analysis + Layers: Restrictions on uses Source: local land use planning and management agencies Map use: display and analysis Layers: + Administrative areas + Cadastral framework (Public Lands Survey System – PLSS) Sources: U.S. Census Bureau, local and regional land surveys Map use: display and analysis Layers: + Ownership and taxation + Parcel boundaries + Survey network Source: local land use planning and management agencies, local land surveys Map use: display and analysis |

- The facilities will be located on land parcels, with compatible land use

- Streams/River should be far enough away from the facility

- Street network will service the facility

Figure 5.1. Simplified entity-relationship diagram showing only entity classes (boxes) with attributes (on the right side after lines), and showing no relationships.

Figure 5.2. Common geospatial data construct types for raster and vector data models.

Based on National Institutes for Standards and Technology (1994) and Zeiler (1999).

Figure 5.3. Physical schema specification for data types depicted using MS Office Visio UML class properties.

Figure 5.4. Land feature dataset package in the Green County conceptual database design.

Figure 5.5. Data type specifications for land parcel data depicted with MS Office Visio UML class properties.

Figure 5.6. ObjectID for the primary key depicted with MS Office Visio UML class properties.

# Text boxes

Parcel

PIN

size

use

Stream/River

section_ID

name

length

Street

Street_seg_ID

name

Section length