## Slide 1: Material compatibility

## Slide 2: What are these tubes tubes made of?
Polypropylene
  High chemical and thermal resistance (autoclavable)
Polystyrene
  Cheaper clear plastic
  Usually for disposable applications
Polycarbonate
  High strength – high speed spins
  Less chemical resistance

## Slide 3: Sample preparation tubes
Color tubes
  Can leech dyes
    Don’t use for MS or optical measurements
Sterile
  Irradiated (gamma radiation)
RNAse/DNAse free
Low retention (Lo Bind) tubes
  Coated to bind less protein
  Recommended for dilute protein solutions
    Proteomic samples
Glass vials
  Amber glass (light sensitive samples)
  Silanized glass (coating)

## Slide 4: Gas cylinders & regulators
Brass
  70% copper, 30% zinc
Stainless steel
  304 - 18% chromium, 8% nickel
  316 - 16% chromium, 8% nickel, 2% molybdenum
    More corrosion resistance & more $$$
Gas purity
  2.0 – 99%
  4.0 – 99.99%
  5.5 – 99.9995%

## Slide 5: Water
Industrial water
  Untreated (not potable)
Deionized (DI)
  Reverse osmosis
  One shared tank for the wing
MilliQ
  Combination of UV irradiation, ion exchange, and graphite stages
  Final step through 0.22 μm membrane
  May still contain a lot of plastic polymers
Optima (LC-MS)
  Removal of most polymers that show up on the mass spec
  Optima UPLC grade (even lower levels of background)

## Slide 6: Filters
Pore size
  0.45µm
  0.22µm (very sterile applications) or MALS
  Molecular weight cut-off (MWCO)
Chemistry
  Polyethersulfone (PES)
    Hydrophilic – low protein binding
  Regenerated cellulose
    Low binding, good chemical resistance
  Nylon
    Some chemical resistance, binds protein
  Polytetrafluoroethylene (PTFE)
    Good chemical resistance
  Lookup Compatibility:
    https://biomedical-innovations.com/Products/Syringe-Filters/Membrane-Compatibility.aspx

## Slide 7: Useful Databases
Cole Parmer Material compability:
  https://www.coleparmer.com/chemical-resistance
Plastics International database:
  https://www.plasticsintl.com/chemical-resistance-chart
US plastics database:
  https://www.usplastic.com/catalog/files/charts/LG%20CC.pdf
Thermo Fisher’s database:
  http://tools.thermofisher.com/content/sfs/brochures/D20480.pdf